Constrained Optimization

ConstrainedOptimization is a UG4 Plugin that provides various algorithms used in a constrained optimization setting.
This document should give a thorough overview on ConstrainedOptimization combined with some usage examples. For first time users, using the plugin is not necessarily straightforward, as many things have to be considered. Especially the required data format of the model output and the optimization solver setup itself may present issues. But usually all these issues can be resolved after the user has grasped the gist of how the plugin is supposed to work.
Therefore, this manual is focused more on the usage of ConstrainedOptimization from a user perspective. For an explanation of how the plugin works internally, you may refer to the doxygen file supplied with the plugin.

# Installation

The newest version of the plugin can be downloaded from https://github.com/CowFreedom/ConstrainedOptimization

While compilation of ConstrainedOptimization has no dependencies, it assumes that the terminal command
$ ugshell
exists and starts a Lua compiler. This is usually satisfied by installing UG4 along with the corresponding environment variables. Experienced users could theoretically not install UG4 and set the environment variable ugshell to refer to any Lua (or even e.g. Python compiler). The rest of this manual assumes, however, that UG4 has been properly installed.
## Adding ConstrainedOptimization to UG4
The installation equals the standard process for adding UG4 plugins described on the ughub GitHub page. Due to the usage of OS specific fgunctions for process generation, the plugin is not necessarily multiplatform. In its current form, the package has been shown to work on Windows 10, Linux Ubuntu, Rasperry Pi OS, Arch Linux, and macOS Mojave 10.14.4. On Windows 10, two compilers were tested, GCC 9.3.0 and Visual Studio v16.3.10. It is assumed that the package also works for older compiler versions that support C++17. On Linux Ubuntu, only GCC was tested. On macOS Mojave the Clang compiler was used. Depending on your version of GCC and Clang, special flags might need to be set during the build process. This is explained below. The utilized Visual Studio compiler has not exhibited such necessities but older versions might.

### GCC
Follow the steps on the ughub GitHub page. If errors occur, proceed with this text. The plugin makes use of C++ std::threads. This might necessitates activating the -pthread flag to the build process for ug4. Within your UG4 install library, go to
cd ug4/ugcore/cmake/
and open
ug_includes.cmake
Now search for
elseif("${CMAKE_CXX_COMPILER_ID}" STREQUAL "GNU")
   add_cxx_flag("-Wall")
   add_cxx_flag("-Wno-multichar")
   add_cxx_flag("-Wno-unused-local-typedefs")
   add_cxx_flag("-Wno-maybe-uninitialized")
and add
add_cxx_flag("-pthread")
to the GNU include statements. Now rebuild UG4 as described on the ughub GitHub page. The plugin should now be installed without any issues.
### Clang
Follow the steps on the ughub GitHub page.. If errors occur, proceed with this text. The plugin makes use of C++11 features, like std::threads and constexpr. This might necessitates activating the -std=c++11 flag to the build process for ug4. Within your UG4 install library, go to
cd ug4/ugcore/cmake/
and open
ug_includes.cmake
Now search for
elseif("${CMAKE_CXX_COMPILER_ID}" STREQUAL "Clang")
    add_cxx_flag("-Wall")
    add_cxx_flag("-Wno-multichar")
and add
set(CMAKE_CXX_FLAGS "${CMAKE_CXX_FLAGS} -std=c++11")
to the Clang include statements. This ensures that the -std=c++11 flag is only added to the C++ compiler and not the C compiler in the build process. Now rebuild UG4 as described on the ughub GitHub page. The plugin should now be installed without any issues.
# Descripton
# The following algorithms are currently implemented:
Name	Description
Newton-Gauss	The Gauss Newton procedure minimizes functions that can be represented as a sum of squares.
Particle Swarm Optimization	The Particle Swarm Optimization (PSO) algorithm minimizes any continuous function on a bounded domain.
Geometry Sampler	Takes random samples from an arbitrary loss function.

The inner workings of each of these algorithms are either self explaining or can be found in publically available lecture. The main feature of ConstrainedOptimization is the compartmentalization of problem formulation, solution finding and the underlying computation mechanism. A problem is formulated via child instantiations of the Evaluation class type, which includes details such as the objective function to be optimized or problem specific parsing details. Solution finding algorithms are represented as classes such as NewtonOptimizer. Computational interaction with UG4 is abstracted away in instances of ComputationMode. Combined, this setup gives a flexible and modular platform that can be adapted for many problems at hand. For a descripton of the inner workings of this plugin, please refer to the doxygen file supplied with the plugin.
# Working example: Fitting disease data to an epidemics model

The following example fits Covid-19 disease data to a partial differential equations model used for epidemiological purposes. First, the real world dataset is presented. Then the epidemiological model trying to explain the real life dataset is described. Then, the data output of the epidemiological model is rearragned into a format that ConstrainedOptimization can understand.
Afterwards, all the necessary files for an optimization of parameters through ConstrainedOptimization are created and the optimization algorithms are run. Lastly, results are discussed. For the entire paper where this exact scheme was used please refer to [Covid Paper].
## Dataset
TODO
## Epidemiological Model
TODO
## Optimization with CO

# FAQ:ُ Error codes and their meanings
# Folder Structure